## Slide 1
Results of Prefeasibility Studies for SHIP installations in Tunisia
Kick-off Opportunity Study 26.09.2014
Dissemination of Innovative Solar Thermal Applications in the Tunisian Industry (DASTII)

## Slide 2
Realisation of one SHIP Installation
Technical trainings, Networks
Information, Communic.
Analysis of Framework Conditions/ Economics
Technology transfer
Knowhow transfer
Dissemination of SHIP installations in the Tunisian industry
Reduction of CO2 Emissions
Regulatory support scheme
The DASTII Project
Awareness raising
Objective
4 Main Approaches
Activities

## Slide 3
SHIP Installation Project
Realisation of a SHIP installation in a Tunisian industrial company
Objectif: Fuel Savings equivalent to 250 t CO2 / year
Utilisation of a concentrating collector technology at medium temperature level (> 150°C)
Potential branches: Food, Beverage, Textile, Chemics, others

## Slide 4
Selection process of industry partner for SHIP Project
1. Preselection | Preselection of 20 industrial companies based on prior analysis (Potential Study) Representation of most relevant branches (Food, Textile, Chemical, Brick)
2. Site Visits | Verification of site conditions, level of interest Collection of technical data via questionnaires  Selection of 5 most favorable candidates
3. Energy Audits | Thermal energy measurements on site Set-up of daily and annual energy demand profile
4. Prefeasibility Study | Techno-economic assessment of SPH integration on 5 sites
5. Feasibility Study | Selection of industry partner through detailed study

## Slide 5
Prefeasibility Study - Assumptions
Energy Prices | 
Nat. Gas Cost [€ct/kWh] | 1,76
Fuel Oil Cost [€ct/kWh] | 2,5
Energy Price Increase per year [%/a] | 10%
Technical Parameters | 
Collector | Fresnel
Optical efficiency | 0,635
Degradation (%) | 0,5
Life Time (a) | 20
O&M costs/ Inv. Costs (%) | 1
Specific Costs (€/m²) | 550
Solar Irradiation | 
DNI (kWh/m²/a) | 1850 (North) 2000 (Center)
Financial Parameters | 
Equity Share | 80%
Debt Share | 20%
Cost of Equity | 14%
Cost of Debt | 8%
Solar plant must save gas/ fuel oil equivalent to 250 t CO2/ year
Payback time for company max. 5 years
Use of concentrating collector
 = 17 ct/kWh in 20 years
Notes: Solar Plant mit x m², um 250t CO2 einzusparen, kostet y, benötigt z Subventionen für 5 Jahre
Bei 10% durchgehend: No subsidies nach 6 Jahren, 17 ct/kWh nach 20 Jahren
Bei 5% ab Jahr 7: weitere 5 Jahre PBP, 7 ct/kWh nach 20 Jahren

## Slide 6
1. Food Production Company
Sector: Food Industry
Location: North Tunisia
Heat source: Fuel Oil
Heat supply: Steam at 180°C
Processes: Drying (110°C), Sterilisation (130°C)
Energy Profile: 24h/d, 7 d/w., 339 d/a
Energy demand: High, fairly constant

## Slide 7
1. Food company - Results
Solar Field size: 1.250 m²
System utilisation: 34%
Solar Fraction: 5%
Total Invest: 740.000 €
Payback Period: 18 years
Required subsidy (PBP = 5 y): 88%
Emission cut = 250 t CO2/a
Notes: Ohne Monitoring costs: - 1 Jahr PBP

## Slide 8
2. Textile Company
Sector: Textile industry
Location: North Tunisia
Heating source: Natural Gas
Heat supply: Steam at 165°C
Processes:Washing (90°C), Whitening (90°C), Dyeing (90°C)
Energy Profile: 16h, 6 d/w., 283 d/a
Energy demand: Medium, fluctuating

## Slide 9
2. Textile company - Results
Solar Field size: 1.850 m²
System utilisation: 29%
Solar Fraction: 10%
Total Invest: 1.070.000 €
Payback Period: 22 years
Required subsidy (PBP = 5 y): 92%
Emission cut = 250 t CO2/a

## Slide 10
3. Tobacco Company
Sector: Tobacco production
Location: Central Tunisia
Heating source: Heavy Fuel
Heat supply: Steam at 180°C
Processes: Humidification (90°C), Drying (90°C)
Production Profile: 10h, 5 d/w., 178 d/a
Daily profile: 5 a.m. – 14:30 p.m.
Energy demand: Low, highly fluctuating

## Slide 11
3. Tobacco company - Results
Solar Field size: 3.150 m²
System utilisation: 12%
Solar Fraction: 25%
Total Invest: 1.780.000 €
Payback Period: 27 years
Required subsidy (PBP = 5 y): 94%
Emissions cut = 250 t CO2/a

## Slide 12
Conclusions
Details on current SHIP system costs and cost distribution
Influence of collector technology, integration method, application (energy profile), storage on economics  Simulation
Identification of potential market niches
Definition of minimum framework conditions for market development
Expected results of the study (Industry sector)
Technical potential for SHIP in Tunisia
Very low energy prices (1/3 – 1/4 of European average)
Low profitability even in favorable cases
Very high subsidy levels necessary

## Slide 13
Frank Münk
Project Manager DASTII
GIZ - Deutsche Gesellschaft für Internationale Zusammenarbeit
Tunis, Tunisia
frank.muenk@giz.de
www.giz.de | www.dastii.com

## Slide 14
Final energy consumption
6,5 Mtoe
Industry
36%
Thermal consumption
74%
Other consumption
26%
Transport
30%
Residential
17%
Service
10%
Agriculture
7%
Construction Material Industry
65%
Chemical industry
10,2
Food Industry
6,9
Mechanical and Electrical Industry
6,6%
Various industries
7,1%
Textile Industry
4,2%
Distribution of Final Energy Consumption (2012)
Cement
Brick
Tobacco
Paper
 Thermal energy demand of industry equals ~25% of national final energy demand

## Slide 15
Selection criteria for identification of partner companies
Cooperative
Level of interest / motivation for project
Environmental
Solar irradiation level (1.800 kWh/m²a +)
CO2 reduction potential (250t/y +)
Financial
Cooperation: Willingness to share operation data and to allow site visits
Financial stability, stable cash-flows
Technical
Estimated solar share (10%)
Type of fuel (Natural gas or fuel oil)
Contribution to plant investment
Available space on site (3.000 m² +)
Production profile (days per week, time per day)
Tolerated roof loads (150 Kg/m²)

## Slide 16
DNI values in Tunisia (source Med Atlas)
GHI levels in Tunisia (source Med Atlas)
Solar irradiation potential in Tunisia
Concentration of industrial sites

## Slide 17
Study trip to Germany/Switzerland for Tunisian energy experts from government agencies
NEP Solar: Cheese dairy in Switzerland
Ritter : Radiator fabrication in Switzerland
Indstrial Solar: Metal fabrication in Germany
4. Awareness raising & communication

## Slide 18
2. Context – The Tunisian Industry and Energy sector

## Slide 19
Total Thermal Consumption
Natural Gas
51,5%
Pet Coke
21,1%
Fuel Oil
21,4%
Gasoil
3,9%
GPL
2,1%
Thermal energy sources of the industry
Costs of Energy
Energy | End user costs (net)
Natural gas | 0,11 €/m3
Gasoil | 0,53 €/litre
Heavy fuel | 218 €/ton
GPL | 503 €/ton
Source: STEG, Tunisian ministry of industry (January 2013)
Subsidies on Natural gas and Fuel oil: ca. 50%
Energy subsidies in 2012: 5,3 Bil. DT
New government strategy: Gradual suspension of subsidies on natural gas starting with the largest energy consumers (Cement industry)
Source: Tunisian Energy Agency

## Slide 20
PROSOL: Residential sector
Target: Residential houses
Application: Hot water preparation
Technology: Solar Water Heater with Flat Plate Collectors
Supply: 50 eligible suppliers, among 9 manufacturers
Subsidy Scheme: 200-400 DT/ unity installed, Credit line
Target: Hotels, Swimming pools, Traditional baths, collectives residences
Application: Hot water preparation
Technology: Solar Water Heater with Flat Plate Collectors, Vacuum Tube collectors
Achievements: 20 installations, 50 hotels engaged
Subsidy Scheme: 30% of investment with cap of 150 DT/m²
50% of costs of feasibility study up to 5.000 DT
PROSOL: Service sector

## Slide 21
PROSOL: Industry sector
Program started 2010 with support of UNDP and Italian Cooperation
SPH potential study (2012):  Analysis of hot water/steam demand (Food, Textile, Chemical and various industries)  No consideration of hot air processes (Construction, Metallurgic)  Site visit and inquiry in 64 companies, extrapolation of results  > 80% of thermal demand for steam production up to 250°C
So far:  No operating SPH plant in Tunisia (One low-temp demo plant in textile industry in planning stage)  Almost no experience with SPH in industry and research
 No appropriate financial support mechanism in place (30% of investment with cap of 150 DT/m²)